DIACOM ®  Diagnostic Status Report

04.19.2007 17:33:30

1. VEHICLE CONFIGURATION

Engine Make:   		62

Engine Serial No:		N/A

Model Year:     		N/A

System Type:   		MerCruiser PCM555

2. PERFORMANCE DATA

Parameter Description              	Value               	Unit

Available Power                    	100                 	%

Baro Pressure                      	100,84              	KPA

Battery Voltage                    	12,30               	VDC

Coolant Temperature                	17,00               	°C

Engine Speed                       	0                   	RPM

Fuel Flow Rate                     	0,00                	LPH

Fuel Level                         	1023                	#

IAC Duty Cycle                     	0,00                	%

Lake/Sea Temp                      	0,00                	°C

Manifold Absolute Pressure         	100,77              	KPA

Manifold Air Temperature           	18,00               	°C

Oil Pressure                       	0,99                	KPA

Paddle Wheel                       	0                   	Hz

Pitot ADC                          	0                   	#

Port Exhst Cool Temp               	0,00                	°C

Sea Pump Pressure                  	0,00                	KPA

Sensor Power                       	5,00                	VDC

Spark Advance                      	8,00                	DEG

Starb Exhst Cool Temp              	0,00                	°C

Throttle Position                  	0,12                	%

Throttle Sensor Voltage            	0,64                	VDC

Trim Position                      	1023                	#

Trim Volts                         	5,10                	VDC

3. TROUBLE CODE STATUS

Current ECM Codes

Sensor Fault, click Read Fault button for details

Trouble Code List:

PITOT CKT LO                  	 Code is active

FUEL LVL CKT HI               	 Code is active

STEER CKT LO                  	 Code is active

SEA TMP CKT HI                	 Code is active

TRIM CKT HI                   	 Code is active

Freeze Frame Data:

0	TRIM CKT HI

--------------------------------------------------------------------

FF Baro Pressure                         	100,72          	KPA

FF Battery Volts                         	12,06           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	15,00           	°C

FF Coolant Temp                          	16,00           	°C

FF Demand                                	0,12            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	233

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	100,74          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,08            	%

FF Available Power                       	100             	%

FF Run Time                              	23,85           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,12            	%

FF Trim Position                         	0,00            	%

1	HORN OUTPUT

--------------------------------------------------------------------

FF Baro Pressure                         	103,13          	KPA

FF Battery Volts                         	9,44            	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	29,00           	°C

FF Coolant Temp                          	45,00           	°C

FF Demand                                	0,63            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	94

FF Fuel Level                            	0,00            	%

FF Gear Position                         	Neutral

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	98,43           	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,31            	%

FF Available Power                       	50              	%

FF Run Time                              	17,68           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,63            	%

FF Trim Position                         	0,00            	%

2	STEER CKT LO

--------------------------------------------------------------------

FF Baro Pressure                         	100,84          	KPA

FF Battery Volts                         	12,06           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	16,00           	°C

FF Coolant Temp                          	16,00           	°C

FF Demand                                	0,12            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	212

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	100,84          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,19            	%

FF Available Power                       	100             	%

FF Run Time                              	23,85           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,12            	%

FF Trim Position                         	0,00            	%

3	SEA TMP CKT HI

--------------------------------------------------------------------

FF Baro Pressure                         	100,84          	KPA

FF Battery Volts                         	12,03           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	16,00           	°C

FF Coolant Temp                          	16,00           	°C

FF Demand                                	0,12            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	197

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	100,84          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,37            	%

FF Available Power                       	100             	%

FF Run Time                              	23,85           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,12            	%

FF Trim Position                         	0,00            	%

4	FUEL LVL CKT HI

--------------------------------------------------------------------

FF Baro Pressure                         	100,84          	KPA

FF Battery Volts                         	12,06           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	16,00           	°C

FF Coolant Temp                          	16,00           	°C

FF Demand                                	0,12            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	194

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	100,84          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,43            	%

FF Available Power                       	100             	%

FF Run Time                              	23,85           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,12            	%

FF Trim Position                         	0,00            	%

5	PITOT CKT LO

--------------------------------------------------------------------

FF Baro Pressure                         	100,84          	KPA

FF Battery Volts                         	12,03           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	16,00           	°C

FF Coolant Temp                          	16,00           	°C

FF Demand                                	0,12            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	195

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32772,0

FF Manifold Air Pressure                 	100,82          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,45            	%

FF Available Power                       	100             	%

FF Run Time                              	23,85           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,12            	%

FF Trim Position                         	0,00            	%

6	LOW DRIVE LUBE

--------------------------------------------------------------------

FF Baro Pressure                         	100,60          	KPA

FF Battery Volts                         	11,71           	VDC

FF Sea Pump Pressure                     	0,25            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	13,00           	°C

FF Coolant Temp                          	13,00           	°C

FF Demand                                	1,13            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	18

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32768,0

FF Manifold Air Pressure                 	100,60          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,05            	%

FF Available Power                       	100             	%

FF Run Time                              	17,68           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	1,13            	%

FF Trim Position                         	0,00            	%

7	ECT TMP CKT HI

--------------------------------------------------------------------

FF Baro Pressure                         	101,93          	KPA

FF Battery Volts                         	12,22           	VDC

FF Sea Pump Pressure                     	0,00            	KPA

FF Boat Speed                            	0,00

FF Manifold Air Temp                     	27,00           	°C

FF Coolant Temp                          	24,00           	°C

FF Demand                                	0,00            	%

FF Engine Speed                          	0               	RPM

FF Engine State                          	Stall

FF FPC Total                             	0,0             	Counts

FF Frequency Count                       	2

FF Fuel Level                            	0,00            	%

FF Gear Position                         	In Gear

FF Lake Temp                             	0,00            	°C

FF Engine Load                           	0,00            	%

FF Main Pwr Relay Requests               	32768,0

FF Manifold Air Pressure                 	101,93          	KPA

FF Oil Level                             	0,00            	%

FF Port Tab Pos                          	0,15            	%

FF Available Power                       	100             	%

FF Run Time                              	16,87           	hrs

FF Starboard Tab Pos                     	0,00            	%

FF TPS Percent                           	0,00            	%

FF Trim Position                         	0,00            	%

Fault Log Data

Fault Descriptions                 		Seconds

Battery Range High:                      	0

Battery Range Low:                       	0

Block Pressure is Low:                   	0

Compressor Temp Overheat:                	0

ETC Motor Open:                          	0

ETC Motor Short:                         	0

Fuel Pressure Sensor Input High:         	0

Fuel Pressure Sensor Input Low:          	0

Guardian Strategy:                       	0

Knock Sensor 1:                          	0

Knock Sensor 2:                          	0

Low Oil Pressure Strategy:               	0

Low Oil Remote Strategy:                 	0

Low Oil Reserve Strategy:                	0

MAP Sensor 1 Input High:                 	0

MAP Sensor 1 Input Low:                  	0

MAP Sensor 1 Idle Rational:              	0

Oil Pump Output:                         	0

Overspeed:                               	0

Port Clnt Overheat:                      	0

Starboard Clnt Overheat:                 	0

Warning Horn Output:                     	10763

Water In Fuel:                           	0

Engine Run Time History:

Total engine run time:	23,85          	Hours

0 -  749 RPM:	4,12           	Hours

750 - 1499 RPM:	1,72           	Hours

1500 - 2999 RPM:	3,53           	Hours

3000 - 3499 RPM:	0,40           	Hours

3500 - 3999 RPM:	0,03           	Hours

4000 - 4499 RPM:	0,00           	Hours

4500 - 4999 RPM:	0,00           	Hours

5000 - 5499 RPM:	0,00           	Hours

Over   5499 RPM:	0,00           	Hours